Operating Systems II : CS3523
Spring 2019

Theory Assignment 1: Chapter 6, 7 from the book

Instructor : Dr. Sathya Peri
Author : Puneet Mangla (CS17BTECH11029)

Solution 1 :

Busy wait semaphore are used for implementation .

1. The full semaphore is initialised as 0 so its minimum is 0 trivially . Semaphore empty is intialised to n and is decreased only by producer when it can produce item by calling wait on it. Since at max n items can be accomodated in buffer producer can call wait only n times so minimum value of empty is also 0.
2. The empty semaphore is initialised as n . It can only be signaled by consumer only when it consumes one item . For empty to be greater than n , consumer has to consume an item when buffer is empty which is not possible hence , its maximim value is n. Semaphore f	ull is intialialised to 0 ans is only signaled by producer	when it produces an item . Whenever it produces an item it calls wait on empty . Since minimum value of empty can be 0 . The full can only be signaled at max n times . Thus its max value is also n.
3. n - 1 ≤ full + empty ≤ n
  The sum can be n-1 when producer
  executes wait(empty) and has not executed the signal(full) yet.

Note :
In case of no busy waiting minimum value for both semaphores is -1	becuase semaphore is decreased first before sleep in that case .

In case there are more than one producers/consumer threads
0 ≤ full + empty ≤ n (busy waiting )
-INF ≤ full + empty ≤ n (no busy waiting )
minimum value of full/empty = -INF (no busy waiting)

Solution 2 :

semaphore queue = 1
semaphore rw_mutex = 1;
semaphore mutex = 1;
int read count = 0;
Writer
while (true) {
wait(queue);
wait(rw mutex);
signal(queue);
. . .
/* writing is performed */
. . .
signal(rw mutex);
}

Reader
while (true) {
wait(queue);
wait(mutex);
read count++;
if (read count == 1)
wait(rw mutex);
signal(queue);
signal(mutex);
. . .
/* reading is performed */
. . .
wait(mutex);
read count--;
if (read count == 0)
signal(rw mutex);
signal(mutex);
}

Solution 3 :

Compare and compare-and-swap works appropriately for implementing	spinlocks . The reason is even if two or more threads enter the	conditional statement the compare and swap is executed atomically .	That impliest all threads can’t exit the while loop together . There can	be at most one thread entering the critical section while other threads	waiting in spinlock.

Solution 4 :

The problem which such implemtation is that it doesn’t ensure that one	thread is not blocking while waiting for the semaphore. If semaphore	value is 1 and two threads came and enter the if statement then wait will	be executed for both but for the first thread it decreases the semaphore	value to 0 and when second thread calls wait it blocks there.